Annex NE

How to Handle Existing Robots & Robot Cells

- Industrial Robots

  - Definitions (to be moved later)

    - New: Robot that was manufactured after the publication date of this standard, meeting the original equipment manufacturers specifications for the model/type.

    - Existing: Robot that was manufactured prior to the publication date of this standard, meeting the original equipment manufacturers specifications for the model/type.

    - Remanufactured: Robots whose used/failed components (including the robot controller) have been replaced with new or used parts, resulting in specifications that differ from the original equipment manufacturer’s specifications at the time of original manufacture and meet the current manufacturer’s or third party’s specification at the time of remanufacture. To be treated like a new robot. Synonyms: Upgraded

    - Refurbished: Robot whose worn-out or failed components were replaced with new or used parts having the same specifications to the original equipment manufacturer’s specifications at the time of original manufacture.  Replacement components may be new or used.  Synonyms: Rebuilt, Reconditioned, Repaired, Overhauled, Restored (restoration).

    - Relocated: Robots in a location different than the originally installed location.  Example: A robot moved to a different location in a plant with no changes to path programming, operation, process, equipment arrangement, or safeguarding.

    - Modified: Robots with added and/or changed components resulting in specifications that differ from the original equipment manufacturers specifications; e.g. faster, slower, stronger, or more accurate, excluding software updates and program changes.

  - Application

The requirements of this standard shall be applied to robot s per 1.2.1 – 1.2.4.  The flowchart and scenarios in Clause 3.0 can be used to help guide your decision.

    - New or Remanufactured Robots

Robots which are new or remanufactured shall comply with Part 1 of this standard.  NOTE: Software updates and changes that do not change the robots specifications are excluded.

    - Refurbished robots

Robots which are refurbished shall comply with the standard in effect on the date of original manufacture and must comply with the minimum criteria as described in ANSI / RIA 15.06-1999, Clause 1.3.4. or CSA Z434, Clause2.5.

    - Relocated robots

Robots which are relocated shall comply with the standard in effect on the date of original manufacture and must comply with the minimum criteria as described in ANSI / RIA 15.06-1999, Clause 1.3.4. or CSA Z434, Clause 10.3.2 & 10.8.5b.  Also a risk assessment1 must be created that focuses in on any hazard created by the robot in it’s the new location.  Note: Some additional Regional requirements may apply.

    - Modified robots

A risk assessment is necessary to determine if the change warrants an upgrade to comply with this Standard and must comply with the minimum criteria as described in ANSI / RIA 15.06-1999, Clause 1.3.4.  Also a risk assessment1 must be created that focuses in on any hazard created by the robot’s modification.

Note 1: This risk assessment is one that looks primarily at the change point and any new or increased hazards caused by the change point.  This change point could be:

| Change Point | Focus |
| --- | --- |
| New location | The focused risk assessment looks at the robot with respect to the new location. Examples include: walls or building columns creating new pinch points, pits near the robot creating new fall hazards, or new hazards created by existing hazardous processes already at the new location. |
| Modification | The focused risk assessment looks at the robot with respect to the modification. Examples include: adding a camera to the EOAT that creates a new pinch point or maybe adding a new camera that does not create any new hazard, lowering or raising the robot from or on to a pedestal reducing or creating a fall hazard (respectively), or changing a servo motor with a stronger one on a primary axis increasing the ‘struck by’ hazard. |

- Industrial Robot Cells

  - Definitions (to be moved later)

    - New: Robot system comprised of newly installed components.  These components could be previously used in other systems.

    - Existing: A robot system comprised of components that were previously installed elements (e.g., EOAT, conveyor, turntable, etc.).

    - Refurbished: A robot cell comprised of components that are worn-out or failed and have been replaced or repaired returning specifications to the original equipment manufacturer specifications at the time of original manufacture.  Replacement components may be new or used but shall meet the original as-manufactured specifications.  Synonyms: Rebuilt, Reconditioned, Repaired, Overhauled, Restored (restoration).

    - Relocated: A robot system in a location different than the originally installed location including integrating a new robot into an existing robot cell/system or relocating existing robots into a new robot cell/system.   Example: Moving an entire robot system to a different location within a plant or to different plant.

    - Reconfigured: A robot system whose components are rearranged so that the layout is different from the original installation.  A robot system might be reconfigured several times over its life; also it might be both reconfigured and relocated at the same time.

    - Modified: A robot system comprised of components with specifications that differ from the original equipment manufacturer’s specifications; e.g. faster, slower, stronger, or more accurate.

  - Application

The requirements of this standard shall be applied per 2.2.1 – 2.2.4   Flowchart 1 and Scenarios (Table 1) can be used to help guide your decision.

    - New Robot Cells

Robot cells which are new shall comply with Part 2 of this standard.  Individual robot cell components may be covered by other applicable consensus standards.

    - Refurbished Robots Cells

Rebuilt or refurbished robot cells shall comply with the respective standard in effect on the date of original manufacture and must comply with the minimum criteria as described in ANSI / RIA 15.06-1999, Clause 1.3.4 (a) & (b) or CSA Z434, Clause2.5.

    - Relocated robot cells

Robot cells which are relocated shall comply with the respective standard in effect on the date of original manufacture and must comply with the minimum criteria as described in ANSI/RIA 15.06-1999, Clause 1.3.4 (a) & (b) or CSA Z434, Clause 2.5.  Also a focused* risk assessment must be created that focuses in on any hazard created by the robot system in it’s the new location.  Note: Some additional Regional requirements may apply.

    - Reconfigured robot cells

Robot cells which are reconfigured shall comply with the respective standard in effect on the date of original manufacture and must comply with the minimum criteria as described in ANSI/RIA 15.06-1999, Clause 1.3.4 (a) & (b) or CSA Z434, Clause 2.5.  Also a risk assessment2 must be created that focuses in on any hazard created by the robot system’s new layout.

    - Modified robot systems and work cells

Modified robot systems shall comply with the respective standard in effect on the date of original manufacture, must comply with the minimum criteria as described in ANSI / RIA 15.06-1999, Clause 1.3.4 (a) & (b), and a risk assessment2 must be created that focuses in on any hazard created by the robot system’s modification.  If the robot system modification utilizes new features allowed in this standard, (e.g., collaborative work or force limiting), the cell must be modified to meet the requirements of the new standard.

Note 2: This risk assessment is one that looks primarily at the change point and any new or increased hazards caused by the change point.  This change point could be:

| Change Point | Focus |
| --- | --- |
| New Location | The focused risk assessment looks at the robot system with respect to the new location. Examples include: walls or building columns creating new pinch points, pits near the robot system creating new fall hazards, or new hazards created by existing hazardous processes already at the new location. |
| New Layout | The focused risk assessment looks at the robot system with respect to the new layout. Examples include: walls or building columns now creating new pinch points, interference with equipment not part of the robot system but within the robot cell. |
| Modification | The focused risk assessment looks at the robot with respect to the modification. Examples include: adding a camera to the EOAT that creates a new pinch point or maybe adding a new camera that does not create any new hazard, lowering or raising the robot from or on a pedestal reducing or creating a fall hazard (respectively), or changing a servo motor with a stronger one on a primary axis increasing the ‘struck by’ hazard. |

- Sample Existing Industrial Robot & Robot System Scenarios

  - While not all inclusive, the following Scenarios in Table 1 cover many situations commonly found throughout industry.

  - The scenarios listed above in Table 1 are further simplified in Table 2.  Table 2 is intended as a quick reference only.  Once a scenario is selected, use Table 1 and the flowchart to help determine the requirements.

  - The Flowchart is intended to guide you through the process of determining the required actions.